## Slide 1: Networking 101 Day 1 Introduction to Networks and Wireshark

## Slide 2: Today’s Objectives
By the end of class, you will be able to:
Define basic networking terms and explain how data is transmitted over the network.
Describe how protocols structure and define the data transmitted over the network.
Outline the OSI Model and explain each layer.
Compare and contrast the OSI and TCP/UDP model.
Capture communication over the network using Wireshark.
Explain the basics of a packet in Wireshark.

## Slide 3: Introduction to Networking

## Slide 4: Where Are we?
Networking is critical for nearly all these roles. A solid understanding of networking is fundamental to almost all cybersecurity.
Security Analyst | Security Operations Center Analyst (SOC) | Security Engineer | Systems Engineer
Cyber Threat Analyst | Cyber Defense Analyst | Incident Response Analyst | Intelligence Analyst
Information Assurance Technician | Risk Analyst | Forensics Investigator | Systems Administrator
Network Engineer | It Auditor | Application Security Engineer | Penetration Tester
Information Analyst | Systems Security Analyst | IT Specialist | Web Engineer - Application Security

## Slide 5: The Journey of a File

## Slide 6
A network is a group of computer systems and computing devices that are linked together through communication channels to facilitate communication and resource sharing among a wide range of users.

## Slide 7: Network Communication: The Client Server Model
Network communication occurs largely between clients and servers.
Notes: Clients can be anything such as a computer, phone, or camera. They may request data such as files, maps, web pages, and images.

## Slide 8: Network Communication: The Client Server Model
Multiple clients often communicate with a single server.
(smart bulb)

## Slide 9: Client / Server Model
A lot of this seems like magic!
The Client sends a request for info to the server.
Client: I’d like file X please
2. The server responds with data.
Server: Here’s file X you asked for
x

## Slide 10: Client / Server Model
But there’s a lot to learn about this “simple” process:
Client: I’d like file X please
Server: Here’s file X you asked for
x
How does the client find the server and vice versa?
How is this request made?
How is it sent?
How is this file found?
How is it sent?

## Slide 11: 10 Minutes Activity: Explaining Communication In this activity, you will pair up and think about how some common tasks might fit into the client / server framework. Instructions sent via Slack

## Slide 12: Activity: Explaining Communication 10 Minutes
Instructions:
With a partner, investigate and explain how each of the following might work in communicating over the network:
File Transfer
Email
Web Page
For each scenario, think about and try to explain each of the following:
Who is the client? The server?
What does the request look like? The response?
What work does the client do? The server?
What is being communicated?
Use Google to help you in your investigation!

## Slide 13: Explaining Communication Review
File Transfer:
The Client sends a request for info to the server.
Client: I’d like file X please
2. The server responds with data.
Server: Here’s file X you asked for
x

## Slide 14: Explaining Communication Review
##AGH58e!@5837FFFfH^#$__R)@J34G(
Web Pages:
User selects a link in the browser.
Browser formats the request and sends it to the server
Server finds the requested web pages.
Server formats the response and sends it to the client (browser).
Browser receives HTML and renders it into a user display
-.--..-.-.-.-.-.-.-.-..
..-..-.-
-.--..-.-.-.-.-.-.-.-..
..-..-.-
Click me
Website
-.--..-.-.-.-.-.-.-.-..
..-..-.-
##AGH58e!@5837FFFfH^#$__R)@J34G(
-.--..-.-.-.-.-.-.-.-..
..-..-.-
##AGH58e!@5837FFFfH^#$__R)@J34G(
-.--..-.-.-.-.-.-.-.-..
..-..-.-
-.--..-.-.-.-.-.-.-.-..
..-..-.-
-.--..-.-.-.-.-.-.-.-..
..-..-.-
##AGH58e!@5837FFFfH^#$__R)@J34G(
-.--..-.-.-.-.-.-.-.-..
..-..-.-
-.--..-.-.-.-.-.- HTML..
..-..-.-

## Slide 15: Explaining Communication Review
Email:
To: peleke@yo.yo
From: nick@yo.yo
Yo Yo Yo! How it go?
To: peleke@yo.yo
From: nick@yo.yo
Yo Yo Yo! How it go?
Client: Sender Nick
Client: Receiver Peleke
Mail Server
For some communication, there may be more than one server behind the scenes doing work.

## Slide 16: Explaining Communication Review
Networking Definitions
Network: A system of computers and other devices (printers, smart objects) that are connected to each other.
Network Communication: Transmission of data between two or more computers over a network.
Client / Server: Multiple end devices (clients) communicating over a network with a single central computer (server)
Request / Response: A basic method of computer communication, in which one computer sends a request for data to a second computer that responds to that request.

## Slide 17: Introduction to Protocols

## Slide 18: Request/Response and Binary
Here’s file X you asked for
I’d like file X please
Here’s file X you asked for
111000100101010100010011100
000110010101101011010111001
000110010101101011010111001
111000100101010100010011100
Here’s file X you asked for
x
x
All digital data is transmitted via binary.

## Slide 19: A Protocol is a set of standardized rules that specify how interactions between communicating entities should work. How networks communicate and provide structure to the binary data that is transmitted.

## Slide 20: Protocol Example: Authentication
PAP: Password Authentication Protocol
Username: Alice
Password: awesomeAlice1
Accept / Reject
Alice’s Personal Computer
Server
PAP Two-Way Handshake

## Slide 21: Protocol Example: Authentication
Client request contains bits in a specific order and length, per the standard and rules of the protocol.
Username: Alice
Password: awesomeAlice1
Accept / Reject
Alice’s Personal Computer
Server
1 Byte | 1 | 2 Bytes | 1 Byte | Variable | 1 Byte | Variable
Code: 1 | ID | Length | User name length | User name | Password Length | Password
Notes: HTTP:80
HTTPS:443
FTP:21
SSH:22

## Slide 22: Protocol Example: Authentication
The server receiving the request will know where to look in the bitstream for content: the username and password.
Username: Alice
Password: awesomeAlice1
Accept / Reject
Alice’s Personal Computer
Server
1 Byte | 1 | 2 Bytes | 1 Byte | Variable | 1 Byte | Variable
Code: 1 | ID | Length | User name length | User name | Password Length | Password

## Slide 23: Ports
Ports are access points used by data that is packaged and interpreted by protocols.
0 - 1023: System Ports
1024 - 49151: Registered Ports
49152 - 65536: Dynamic / Private Ports

## Slide 24: Source / Destination Ports
Source Port: Randomly generated from unregistered port range
Destination Port: Dependent on the protocol
“I’d like cat.jpg please”
151.20.0.145
Port 80
188.4.4.72
Port 50158
OK. Here’s the file you asked for:
Notes: Cat Shutterstock ID: 1041783286

## Slide 25: 10 Minutes Activity: Ports and Protocols In this activity, you will identify the correct port number and functions for a given list of protocols. Instruction sent via Slack.

## Slide 26
Ports and Protocols

## Slide 27: Today’s Objectives: Checkpoint
By the end of class, you will be able to:
Define basic networking terms and explain how data is transmitted over the network.
Describe how protocols structure and define the data transmitted over the network.
Define the OSI Model and explain each layer.
Compare and contrast the OSI and TCP/UDP model.
Capture communication over the network using Wireshark.
Explain the basics of a packet in Wireshark.

## Slide 28: The OSI Model

## Slide 29: The Open Systems Interconnection (OSI) Model
The OSI Model provides a framework to better categorize and conceptualize the overwhelming volume of ports and protocols.
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
The OSI Model depicts the travel of communication through 7 layers, slowly growing the data frame to incorporate aspects like protocol information, security measures, and other pertinent information.

## Slide 30: OSI Model
Layer 7
Layer 6
Layer 5
Layer 4
Layer 3
Layer 2
Layer 1
Layer 7
Layer 6
Layer 5
Layer 4
Layer 3
Layer 2
Layer 1
Application 1
Application 2
UserData
UserData
UserData
Data Frame
Additional data in the Frame added for security, addressing, etc.
Only the actual user data is presented to the application
UserData
UserData
UserData
Data Frame
Eg. Profibus, DeviceNet, Ethernet
Only the user data is presented to the application
Network Cable

## Slide 31: OSI Model
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
Data Received
Data Transmitted
[Physical Link]
Data
Data
Data
Segments
Packets
Frames
Bits

## Slide 32: The OSI Model: Physical Layer
The Physical Layer is responsible for transmission of binary data via a physical medium. Handles how data is physically encoded and decoded.
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application

## Slide 33: The OSI Model: Data Link
The Data Link layer establishes links between nodes and provides error-free handling of data transfer over the Physical layer.
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application

## Slide 34: The OSI Model: Network Layer
The Network layer is responsible for routing data through physical networks, deciding which physical path the data will take, and ensure that it gets to the correct destination.
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application

## Slide 35: The OSI Model: Transport
The Transport Layer is responsible for actually transmitting data across the network. (It puts data onto the network.)
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application

## Slide 36: The OSI Model: Session Layer
The Session Layer manages connections between ports on computers and handles data flow.
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application

## Slide 37: The OSI Model: Presentation Layer
The Presentation layer is the translator for the network. It formats the data to be presented to the Application layer. Handles data representation, de/encryption, character set translation and conversion.
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application

## Slide 38: The OSI Model: Physical Layer
The Application Layer is responsible for representing data in a way the consuming application can understand.
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
Website

## Slide 39: Encapsulation / Decapsulation
Encapsulation converts data from an application on the source machine (like an image) into some that can be transmitted.
User data converted for transmission
Upper layer data
Upper layer data
Upper layer data
Upper layer data
TCP Header
TCP Header
TCP Header
FCS
IP Header
IP Header
LLC header
MAC header
111010101111101101001100101010 → Sent to cable
Network Media
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 40: Encapsulation / Decapsulation
Decapsulation converts transmitted data into something that can be used on the destination's machine application.
User data converted for transmission
Upper layer data
Upper layer data
Upper layer data
Upper layer data
TCP Header
TCP Header
TCP Header
FCS
IP Header
IP Header
LLC header
MAC header
111010101111101101001100101010 → Sent to cable
Network Media
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 41: OSI Model
Twitter OSI Model
Physical Layer: You just thought of a tweet that you need to share with the world, so you whip out your smartphone.
Data Link Layer: Your 280 character tweet is converted into binary 1s and 0s.
Network Layer: Your tweet is routed over various LAN and WANs. (Directing your tweet’s travel path).
Transport Layer: Packs up your 280 character tweet and sends it into the Twittershpere.
Session Layer: Provides order to a session. Like the traffic cop of data between transfers.
Presentation Layer: Translates binary 1s and 0s into a comprehensible format.
Application Layer: Your tweet is ready to be viewed by the world!

## Slide 42: TCP / IP Model
The Transport Control Protocol / Internet PRotocol Model is another model, more in accordance with cybersecurity issues.
Layer 1: Physical
Layer 2: Data Link
Layer 3: Network
Layer 4: Transport
Layer 5: Session
Layer 6: Presentation
Layer 7: Application
Host-To-Network Layer
Internet Layer
Transport Layer
Application Layer

## Slide 43: 10 Minutes Activity: Fill in the Blanks In this activity, you will practice familiarizing yourself with the OSI model. Instructions sent via Slack.

## Slide 44
Fill in the Blanks

## Slide 45: Take A Break

## Slide 46: Intro to Wireshark

## Slide 47: Packets and Wireshark
Communication between devices over a network is facilitated through the transfer of packets.
Wireshark is a tool that allows us to look at real communication across the network and monitor the network for activities of connected devices.

## Slide 48: Packets
Communication between devices over a network is facilitated through the transfer of tiny packets.
Application
Presentation
Session
Transport
Network
Data Link
Physical
Data
Data
Data
Segments
Packets
Frames
Bits
Header | Sender’s IP Address, Receiver’s IP Address, Protocol... | 96 bits
Payload | Data | 660 bits
Trailer | Indicates end of packet, error correction | 32 bits
Each packet contains:
The address of its origin
The address of its destination
Some information that connects it to related packets being transmitted

## Slide 49: Packets
Communication between devices over a network is facilitated through the transfer of tiny packets.
Application
Presentation
Session
Transport
Network
Data Link
Physical
Data
Data
Data
Segments
Packets
Frames
Bits
Header | Sender’s IP Address, Receiver’s IP Address, Protocol... | 96 bits
Payload | Data | 660 bits
Trailer | Indicates end of packet, error correction | 32 bits

## Slide 50: 5 Minutes Activity: Install Wireshark In this activity, you will install the wireshark application. Instruction sent via Slack.

## Slide 51: Wireshark Walkthrough

## Slide 52: 10 Minutes Activity: Diving with the Wiresharks In this activity, you will conduct a capture, investigate a packet capture files, and answer a series of questions about the traffic in a file. Instruction sent via Slack.

## Slide 53: Inspecting a Packet

## Slide 54: 10 Minutes Activity: My First Sniff In this activity, you complete your own practice capture. Instruction sent via Slack.

## Slide 55: Today’s Objectives
By the end of class, you will be able to:
Define basic networking terms and explain how data is transmitted over the network.
Describe how protocols structure and define the data transmitted over the network.
Define the OSI Model and explain each layer.
Compare and contrast the OSI and TCP/UDP model.
Capture communication over the network using Wireshark.
Explain the basics of a packet in Wireshark.
Any Questions?